## Slide 1: FPGA Workshop
Dock18 – 7 & 8 October 2017

## Slide 2: FPGA? PROM vs PAL vs FPGA
Programable Read-Only Memory (PROM) and Programable Array Logic (PAL)
  One time programable, burning fuses
  Combination of an AND Array and an OR Array
PROM vs PAL
  AND Array fix vs OR Array Fix

## Slide 3: FPGA? PROM vs PAL vs FPGA
Field Programable Gate Array
  SRAM based, needs programing after power cycle
  Combination of a Logic Cell Array and Connection Matrix
Logic Cell (simplified)
  4 Input, 1 Output, CLK, RST, LUT, FF, MUX,
  Programable LUT and MUX

## Slide 4: FPGA? PROM vs PAL vs FPGA
Switching Matrix (simplified)
  N-Input, N-Output, 1 to N connection
  Programable Transistor Array

## Slide 5: FPGA? PROM vs PAL vs FPGA
Combination of both
  Logic Cells connected to Switching Matrix and then to Logic Cells again …

## Slide 6: FPGA? PROM vs PAL vs FPGA
With these two building blocks basically all digital designs can be built
Same FPGA can be used for many purposes
  PWM Generator
  I2C Controller
  Serial Transceiver
  Softcore CPU
  Digital Filter
  Coprocessors (Encryption, Calculations etc.)
  Etc.

## Slide 7: FPGA? PROM vs PAL vs FPGA
Todays FPGAs have between a couple of 1000 and a couple of 100000 Logic Cells
  DE0 Nano 22320 Logic Cells
But today FPGAs contain much more than just Logic Cells and Switching Matrixes
  Block RAM
  DSP Slices
    Multiplier and Adder
  PLLs
  Gigabit Transceivers
  Clock Networks
  Etc.

## Slide 8: FPGA? PROM vs PAL vs FPGA
FPGA has to be loaded after Powercycle
  Config Flash which stores the configuration for the FPGA which is fetched by the FPGA at boot time
  Pushing configuration via JTAG

## Slide 9: FPGA? MCU vs FPGA
MCU processes instruction sequencialy
  Program is a list of instructions and data
  CPU processes one instruction after the other
FPGAs process «instructions» in parallel
  «Program» is a describtion of the hardware
  All Logic Cells and Switching Matrixes are active at the same time
  Sequencializing of tasks with statemachines or pipelines

## Slide 10: FPGA? How do I program that thing?
Old and very inefficient:
  Instantion of building blocks and connecting them
  Either graphical or in a programing language

## Slide 11: FPGA? How do I program that thing?
Modern, and how we are doing it:
  With a Hardware Description Language: VHDL

## Slide 12: VHDL? What is this?
Very High Speed Integrated Circuit Hardware Description Language (VHDL)
  Syntax based on ADA
    Very very type strict!
  Describe the desired behaviour and let the FPGA tool figure out what building blocks it needs and how to connect them
  Abstracts the internals from the functionality

## Slide 13: Developing an FPGA Design? How does it work?
Couple of different inputs needed:
  VHDL Design
    Defines what the FPGA shall do
  Pinout Constraints
    Defines which Input and Output pins shall be used by the VHDL Design
  Timing Constraints
    Defines the timely behaviour of external interfaces and defines timing maxima internaly

## Slide 14: Developing an FPGA Design? How does it work?
Analyser & Synthesiser:
  Analyses the source code and converts VHDL code into building blocks
  Output can be again a VHDL file which only contains instatiation of FPGA primitives
Fitter (Place and Router)
  Places the FPGA primitives into individual Cells
  Interconnects the Cells via the Switching Matrix
  Takes the Pinout and Timing Constraints into account, where bestto place Logic and how to interconnect them

## Slide 15: Developing an FPGA Design? How does it work?
Assembler:
  Converts the configuration of each Logic Cell and Switching Matrix in one so called Bitstream which is in the end the Programming File which is loaded into the FPGAs SRAM which is defining the functionality.
Programmer:
  Allows to configure the Bitstream via USB to JTAG into the FPGA
Timing Analyser:
  Checks if the internal and external timing is fullfiled

## Slide 16: Developing an FPGA Design? How does it work?
Simulator:
  Simulates in software the behaviour based on the source code to verify the functionality
  Needs a so called Testbench which instantiates the design an stimulates the inputs and checks the outputs

## Slide 17: Developing an FPGA Design? How does it work?
Most steps provides input for the next step
There are more tools which make FPGA development and debugging easier

## Slide 18: VHDL Basics What is all that code?
Things happen in parallel but result in one clock cycle is only available in the next cycle!

## Slide 19: VHDL Basics What is all that code?
VHDL has statements which can be used for simulation only
  File operations
  Others like: wait for 100 ms
  Etc.

## Slide 20: Let’s get our hands dirty!
Enough theory, let’s get our hands dirty with our first project!

## Slide 21: DE0 Nano Board

## Slide 22: Project constraints
Some points to simplify things:
  Keep the names of the entities the same as I
  Keep the names of the inputs and outputs the same as I
  Use the same protocol for our Transceiver
  If you have a question ask imediately, it might be interesting to others as well and keeps you from loosing track and time
  After the first project copy that folder an rename it, you don’t want to start the whole project wizard again from scratch

## Slide 23: Project Button and LED
We create a first FPGA design and see how the design flow is and how we can put some stupid logic in the FPGA, clocked and combinatorical
What we will do:
  Create a first Quartus Project
  Create a first VHDL File
  Create Pinout Constraints
  Create Timing Constraints
  Make a first design run and configure the FPGA
  Advance the Design
  See a testbench example

## Slide 24: Project LED PWM
We create a Pulse Width Modulator to have different brightness on LEDs and we create a Knightrider pattern on the LEDs
What we will do:
  Create a PWM generator
  Create a Knightrider pattern generator
  See another testbench

## Slide 25: Project Transceiver
We create a transceiver which transfers its own LED pattern to another ones DE0 Nano via a serial interface and display the received LED pattern.
What we will do:
  Create a Transmitter
  Create a Receiver
  See another testbench
  Put all together

## Slide 26: Project Accelerometer (maybe)
Make use of the accelerometer on the DE0 Nano to create a spirit level (Wasserwaage).
What we will do:
  We integrate the I2C acceloremeter and LED geneator and try to understand what’s going on